CWC AD1520 Vortex Recorder

(cwc DRCV)

User Guide

Clement Lee

# Hardware Overview

The cwcDRCV is an intermediate frequency (IF) sampling receiver. It was designed to accommodate GSSR IFs at 325MHz and 460MHz. Make sure the cwcDRCV has a clock connected and set to 1280MHz, 0dBm (10dBm max). Analog input range is 700mVp-p. The trigger input is LVPECL.

# Data Taking

For GSSR:

- Log into 158.154.2.147.

For AO:

- To turn on the receiver, goto http://192.231.95.52/ from a web browser and toggle the port labeled cwcDRCV (6) and Amplifier (1).

- The clock can be accessed at http://192.231.95.53/default.html.

- Log into clement@192.231.95.51{jpl->ao}.

Make sure to add ‘/home/clement/bin’ to your path. NTP should be running on the computer. The timestamp data file names are dependent on the computer time. At the prompt, type ‘cwcDRCV.’

{@prompt}$ cwcDRCV

MENU

1.  Manual Record Now (after 5 sec)

2.  Auto Seq

3.  Stop Manual Record or Auto Seq

4.  Erase File

5.  Erase All File

6.  Get Directory

7.  Get Disk Groups

8.  Get Free Space

9.  Get Status

10. Set Mode

11. Get Mode

12. Perform Readback (RTFS to local)

13. Display Menu

14. UDP Socket

15. Toggle IF

16. Toggle dual

17: Check histogram

-1. Quit

>>

To set mode, enter ‘10’. A table will appear to guide you on what value to set for what IF, output sample rate, and number of channels to record. The numbers in red indicate the mode with the appropriate gain to use. Note 5MHz filter cutoff does not have a steep slope, so output will be noisier.

| 325MHz IF | Dual CH | CH1 only |
| --- | --- | --- |
|  | x1 | x2 | x4 | x1 | x2 | x4 |
| 80MHz | 16 | 48 | 112 | 0 | 32 | 96 |
| 40MHz | 17 | 49 | 113 | 1 | 33 | 97 |
| 20MHz | 18 | 50 | 114 | 2 | 34 | 98 |
| 10MHz | 19 | 51 | 115 | 3 | 35 | 99 |
| 5MHz* | 20 | 52 | 116 | 4 | 36 | 100 |
| 160MHz | 21 | 53 | 117 | 5 | 37 | 101 |

| 460 MHz IF | Dual CH | CH1 only |
| --- | --- | --- |
|  | x1 | x2 | x4 | x1 | x2 | x4 |
| 80MHz | 24 | 56 | 120 | 8 | 40 | 104 |
| 40MHz | 25 | 57 | 121 | 9 | 41 | 105 |
| 20MHz | 26 | 58 | 122 | 10 | 42 | 106 |
| 10MHz | 27 | 59 | 123 | 11 | 43 | 107 |
| 5MHz* | 28 | 60 | 124 | 12 | 44 | 108 |
| 160MHz | 29 | 61 | 125 | 13 | 45 | 109 |

Use check histogram function to check levels.

To record bistatic or loopback, enter ‘1’, followed by duration for recording.

To enable auto sequencing via serial port interface, enter ‘2.’ If /dev/ttyS0 does not have read/write permissions, you will receive an error. This can be corrected by logging in a root and using the following command:

{@prompt}# chmod a+rw /dev/ttyS0

The serial port expects to parse the following:

“start=hhmmss secs=x”

“stop”

To exit auto-sequencing or to cancel a manual recording, enter ‘3.’

To enable UDP Socket sequencing enter ’14.’ And to quit UDP socket sequencing, enter again ’14.’ UDP interface expects the following commands

“take x seconds of data starting at time hhmmss”

“stop”

When finished, enter ‘-1’ to quit program.

# Data Processing

To see the data on the Switched Bunch of Disks (SBOD),

{@prompt}$ FCBls

To see the data from a specific day, on the SBOD,

{@prompt}$ FCBls YYYYMMDD

YYYYMMDD would be the date, for example: 20140504

To get file, enter the filename, which has time stamp:

{@prompt}$ FCBcopy dataYYYYMMDDhhmmss

To get a batch of files, use a start date/time and end date/time:

{@prompt}$ FCBget YYYYMMDDhhmmss YYYYMMDDhhmmss

Processing software:

# Notes

The output data for dual channel

Each 32 bit word is:

| 32 bits (present sample) | 32 bits (next sample) |
| --- | --- |
| schar | schar | schar | schar | schar | schar | schar | schar |
| I1 | Q1 | I2 | Q2 | I1 | Q1 | I2 | Q2 |

The output data for channel 1 only

Each 32 bit word is:

| 16 bits (1st sample) | 16 bits (2nd sample) | 16 bits (3rd sample) | 16 bits (4th sample) |
| --- | --- | --- | --- |
| schar | schar | schar | schar | schar | schar | schar | schar |
| I | Q | I | Q | I | Q | I | Q |

For help, contact clement at clement@jpl.nasa.gov.