29oct18
We have several questions.
1. How things are goung with pump radiation timetable programming? DO you need any additional help?
2. What time shall we inform  you (how long before) about an order of our programs on 7th and 8th of November? Our preferences are: Prog.4  -  from 14:30 till 15:30
                                                           Prog. 1 - from 15:30 till 16:15
                                                          Prog. 2 - from 16:15 till 19:30
                                                          Prog. 3 - from 19:30 till 21:30 (or till the fall of foF2)
Is it possible?
3. We would like to change Program 2. Namely, we'd like to devide this part (60 min) 

Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics, Ionosond
1 min pulse sequence repeats (60 minutes - 60 cycles):
  0:05 pulse train: 160 ms @ 0 ms delay, 200 ms IPP + 200 μs @ 180 ms delay, 200 ms IPP
  0:55 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 μs @ 180 ms delay, 200 ms IPP
 
by two parts, 30 mins each. Namely, the first part is 
Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics, Ionosond
1 min pulse sequence repeats (30 minutes - 30 cycles):
  0:05 pulse train: 160 ms @ 0 ms delay, 200 ms IPP + 200 μs @ 180 ms delay, 200 ms IPP
  0:55 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 μs @ 180 ms delay, 200 ms IPP
The second part is:
Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics, Ionosond
1 min pulse sequence repeats (30 minutes - 30 cycles):
  0:15 pulse train: 160 ms @ 0 ms delay, 200 ms IPP + 200 μs @ 180 ms delay, 200 ms IPP
  0:45 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 μs @ 180 ms delay, 200 ms IPP
Is it possible?

4. Just in case: is it possible to change time shedule (inside the program), i.e. pulse duration and IPP between 7 and 8 November?

5. What the timetable will be used for ISR? How is it sinchronized with the pump radiation timetable? Who can answer detailed questionabout this?