----------------------------------------------
*Programme 1.*  *(15:30 =E2=80=93 16:15 LT)*

1:00 100 usec pulse, 100 ms IPP
                                       we not use ISR data, but it's  OK if
ISR works
0:30 OFF
2:00 5 ms pulse@ (*10-4-D0=3D5.8*) ms delay relative to t0, 2 s IPP
            0 ms delay relative to t0 (1sec tic), IPP-10 ms
0:30 OFF
2:00 10 ms pulse@ (*10-2-D0=3D7.8*) ms delay relative to t0,  2 s IPP
            0 ms delay relative to t0 (1sec tic), IPP-10 ms

0:30 OFF
4:00 20 ms @ (*10-6-D0=3D3.8*) ms delay  relative to t0,  4 s IPP
           0 ms delay relative to t0 (1sec tic), IPP-10 ms
0:30 OFF
10:00 50 ms pulse, @ (*10-2-D0=3D7.8*) ms delay relative to t0,  10 s IPP
          0 ms delay relative to t0 (1sec tic), IPP-10 ms
0:30 OFF
20:00 100 ms pulse, @ (*10-8-D0=3D1.8*) ms delay relative to t0,  20 s IPP
          0 ms delay relative to t0 (1sec tic), IPP-10 ms
0:30 OFF
1:00 100 usec pulse, 100 ms IPP
                        we not use ISR





*FOR Progs. 2 -3. HF:*

*(10-5.2-D0=3D4.6) ms is the initial additional delay for all hf pulses
relative to t0 (1sec tic)!!!*



*ISR pusle:  Coded Long Pulse (CLP) with a duration of 440us (300 m
resolulion) and IPP=3D10 ms, 0 ms delay relative to t0 (1sec tic). The ISR
program   remains unchanged during whole Prog. 1,2,3*



*Programme 2* , experiment (ii) *(16:15 =E2=80=93 18:45 LT)*
Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
30 s pulse sequence repeats (30 minutes - 60 cycles):
  0:01 pulse train: *165 ms* @ 0 ms delay, 200 ms IPP + 200 =CE=BCs @ *185*=
 ms
delay, 200 ms IPP
  0:29 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 =CE=BCs @ *185* ms
delay, 200 ms IPP

Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
1 min pulse sequence repeats (*30 minutes - 30 cycles*):
  *0:05 pulse* train: *165 ms* @ 0 ms delay, 200 ms IPP + 200 =CE=BCs @ *18=
5 *ms
delay, 200 ms IPP
  *0:55 pulse* train: 10 ms @ 0 ms delay, 1 sec IPP + 200 =CE=BCs @ *185* m=
s
delay, 200 ms IPP



Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
1 min pulse sequence repeats (*30 minutes - 30 cycles*):
  *0:15 pulse* train: *165 ms* @ 0 ms delay, 200 ms IPP + 200 =CE=BCs @ 180=
 *185*ms
delay, 200 ms IPP
 * 0:45 pulse* train: 10 ms @ 0 ms delay, 1 sec IPP + 200 =CE=BCs @ *185* m=
s
delay, 200 ms IPP


Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
7.5 min pulse sequence repeats (60 minutes - 8 cycles):
  1:00 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 =CE=BCs @ *185* ms
delay, 200 ms IPP
  2:30 pulse train: *165 ms* @ 0 ms delay, 200 ms IPP + 200 =CE=BCs @ *185*=
 ms
delay, 200 ms IPP
  3:00 pulse train: 10 ms @ 0 ms delay, 1 sec IPP + 200 =CE=BCs @ *185*ms d=
elay,
200 ms IPP
  1:00 OFF

*Programme 3*, experiment (iii) *(18:45 =E2=80=93 21:30 LT)*
Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
6 min pulse sequence repeats (120 minutes - 20 cycles):
  3:00 pulse train: *165 ms* @ 0 ms delay, 200 ms IPP + 200 =CE=BCs @ *185*=
 ms
delay, 200 ms IPP
  3:00 pulse train: 30 ms @ 0 ms delay, 3 sec IPP + 200 =CE=BCs @ *185 *ms
delay, 200 ms IPP

*Programme 4,* experiment (iv) *(14:30 =E2=80=93 15:25 LT)*
Description: 5.1 MHz, *X-mode*, full power, vertical beam, Ionosond
30 sec pulse sequence repeats (25 minutes - 50 cycles):
  10 sec pulse train: 70 ms pulse, 100 ms IPP + 50usec pulse @ 90 ms delay,
100 ms IPP
  20 sec pulse train: 50 usec pulse @ 10 ms delay, 20 ms IPP
  5:00 *change X-mode to O-mode*

Description: 5.1 MHz, O-mode, full power, vertical beam, ISR diagnostics,
Ionosond
30 sec pulse sequence repeats (25 minutes - 50 cycles):
  10 sec pulse train: 70 ms pulse, 100 ms IPP + 50 =CE=BCs pulse @ 90 ms de=
lay,
100 ms IPP
  20 sec pulse train: 50 =CE=BCs pulse @ 10 ms delay, 20 ms IPP